## Slide 1: SECURED WIRELESS COMMUNICATION

## Slide 2: Overview
This project revolves around the establishment of a secured wireless communication channel between two parties.
A half-duplex communication
Messages encrypted end-to-end
The technology employed is Radio Frequency (RF). Microcontroller ATMEGA32 is used which is interfaced with a keyboard through PS2 port to enter data, an RF module, and a standard 16X2 LCD display where the data is displayed. The encryption technology used is Blowfish Algorithm.

## Slide 3: Tasks Accomplished (Progress till the Date)
Much of our time was spent on study of background theory, hardware components, and programming for ATMEGA32. Till the date, the tasks that have been completed are:
Interfacing LCD display
Interfacing RF module

## Slide 4: LCD Interfacing
Standard 16X2 LCD display
Interfaced in 4-bit mode

## Slide 5: UART
Universal Asynchronous Reciver Transmitter
Data is transferred from the data bus to the transmitting UART devices
Adds a start bit, a parity bit, and a stop bit, creating the data packet and data packet is output serially, bit by bit at the Tx pin
The receiving UART reads the data packet bit by bit at its Rx pin and converted the data back into parallel form and removes the start bit, parity bit, and stop bits.
Packet is send serial with the help of SYNC characters

## Slide 6: RF module
An Amplitude Modulating device
Uses USART communication Technique
Implemented asynchronous communication technique
Use of SYNC character for knowing start of transfer and end of transfer

## Slide 7: Interfacing RF as UART devices

## Slide 8: For Receiving End

## Slide 9: Encryption
Used Blowfish Algorithm for data encryption
Open source

## Slide 10: Works Remaining
Interfacing keyboard
Corresponding receiving system

## Slide 11: Applications
Our project can be expanded and optimized to provide the following real-world applications:
Military applications for communicating critical information
Secure communication channel can be used in smart home systems
Useful in message privacy